# References to IT420 class

IP - abbreviation of Internet Protocol. IP specifies the format of packets, also called datagrams, and the addressing scheme. Most networks combine IP with a higher-level protocol called Transport Control Protocol, which establishes a virtual connection between a destination and a source. IP by itself is something like the postal system. It allows you to address a package and drop it in the system, but there's no direct link between you and the recipient. TCP/IP, on the other hand, establishes a connection between two hosts so that they can send messages back and forth for a period of time. The current version of IP is IPv4. A new version, called IPv6 or IPng, is under development.

TCP - abbreviation of Transmission Control Protocol, and pronounced as separate letters. TCP is one of the main protocols in TCP/IP networks. Whereas the IP protocol deals only with packets, TCP enables two hosts to establish a connection and exchange streams of data. TCP guarantees delivery of data and also guarantees that packets will be delivered in the same order in which they were sent.

Hashing produces hash values for accessing data or for security. A hash value (or simply hash) is a number generated from a string of text. The hash is substantially smaller than the text itself, and is generated by a formula in such a way that it is extremely unlikely that some other text will produce the same hash value. Hashes play a role in security systems where they're used to ensure that transmitted messages have not been tampered with. The sender generates a hash of the message, encrypts it, and sends it with the message itself. The recipient then decrypts both the message and the hash, produces another hash from the received message, and compares the two hashes. If they're the same, there is a very high probability that the message was transmitted intact. Hashing is also a common method of accessing data records. Consider, for example, a list of names:

- John Smith

- Sarah Jones

- Roger Adams

To create an index, called a hash table, for these records, you would apply a formula to each name to produce a unique numeric value. So you might get something like:

- 1345873 John smith

- 3097905 Sarah Jones

- 4060964 Roger Adams

Then to search for the record containing Sarah Jones, you just need to reapply the formula, which directly yields the index key to the record. This is much more efficient than searching through all the records till the matching record is found.

Function –

(1) In programming, a named section of a program that performs a specific task. In this sense, a function is a type of procedure or routine. Some programming languages make a distinction between a function, which returns a value, and a procedure, which performs some operation but does not return a value.

Most programming languages come with a prewritten set of functions that are kept in a library. You can also write your own functions to perform specialized tasks.

(2) The term function is also used synonymously with operation and command. For example, you execute the delete function to erase a word.

Hash function- is a process that maps a variable block or message into a fixed-length value called hash code. The function is designed in such a way that, when protected, it provides an authenticator to the data or message known as message digest.

Cryptography- the art of protecting information by transforming it (encrypting it) into an unreadable format, called cipher text. Only those who possess a secret key can decipher (or decrypt) the message into plain text. Encrypted messages can sometimes be broken by cryptanalysis, also called code breaking, although modern cryptography techniques are virtually unbreakable. As the Internet and other forms of electronic communication become more prevalent, electronic security is becoming increasingly important. Cryptography is used to protect e-mail messages, credit card information, and corporate data. One of the most popular cryptography systems used on the Internet is Pretty Good Privacy because it's effective and free. Cryptography systems can be broadly classified into symmetric-key systems that use a single key that both the sender and recipient have, and public-key systems that use two keys, a public key known to everyone and a private key that only the recipient of messages uses.

Digital Certificate -an attachment to an electronic message used for security purposes. The most common use of a digital certificate is to verify that a user sending a message is who he or she claims to be, and to provide the receiver with the means to encode a reply. An individual wishing to send an encrypted message applies for a digital certificate from a Certificate Authority. The CA issues an encrypted digital certificate containing the applicant's public key and a variety of other identification information. The CA makes its own public key readily available through print publicity or perhaps on the Internet. The recipient of an encrypted message uses the CA's public key to decode the digital certificate attached to the message, verifies it as issued by the CA and then obtains the sender's public key and identification information held within the certificate. With this information, the recipient can send an encrypted reply. The most widely used standard for digital certificates is X.509.

IPSec- Short for IP Security, a set of protocols developed by the IETF to support secure exchange of packets at the IP layer. IPsec has been deployed widely to implement Virtual Private Networks (VPNs). IPsec supports two encryption modes: Transport and Tunnel. Transport mode encrypts only the data portion (payload) of each packet, but leaves the header untouched. The more secure Tunnel mode encrypts both the header and the payload. On the receiving side, an IPSec-compliant device decrypts each packet. For IPsec to work, the sending and receiving devices must share a public key. This is accomplished through a protocol known as Internet Security Association and Key Management Protocol/Oakley (ISAKMP/Oakley), which allows the receiver to obtain a public key and authenticate the sender using digital certificates.

SSL - Short for Secure Sockets Layer, a protocol developed by Netscape for transmitting private documents via the Internet. SSL works by using a public key to encrypt data that's transferred over the SSL connection. Both Netscape Navigator and Internet Explorer support SSL, and many Web sites use the protocol to obtain confidential user information, such as credit card numbers. By convention, URLs that require an SSL connection start with https: instead of http. Another protocol for transmitting data securely over the World Wide Web is Secure HTTP (S-HTTP). Whereas SSL creates a secure connection between a client and a server, over which any amount of data can be sent securely, S-HTTP is designed to transmit individual messages securely. SSL and S-HTTP, therefore, can be seen as complementary rather than competing technologies. Both protocols have been approved by the Internet Engineering Task Force (IETF) as a standard.

SMIME- short for Secure/MIME, a new version of the MIME protocol that supports encryption of messages. S/MIME is based on RSA's public-key encryption technology.

It is expected that S/MIME will be widely implemented, which will make it possible for people to send secure e-mail messages to one another, even if they are using different e-mail clients.

MIME -short for Multipurpose Internet Mail Extensions, a specification for formatting non-ASCII messages so that they can be sent over the Internet. Many e-mail clients now support MIME, which enables them to send and receive graphics, audio, and video files via the Internet mail system. In addition, MIME supports messages in character sets other than ASCII. There are many predefined MIME types, such as GIF graphics files and PostScript files. It is also possible to define your own MIME types. In addition to e-mail applications, Web browsers also support various MIME types. This enables the browser to display or output files that are not in HTML format. MIME was defined in 1992 by the Internet Engineering Task Force (IETF). A new version, called S/MIME, supports encrypted messages.

Public key encryption -a cryptographic system that uses two keys -- a public key known to everyone and a private or secret key known only to the recipient of the message. When John wants to send a secure message to Jane, he uses Jane's public key to encrypt the message. Jane then uses her private key to decrypt it. An important element to the public key system is that the public and private keys are related in such a way that only the public key can be used to encrypt messages and only the corresponding private key can be used to decrypt them. Moreover, it is virtually impossible to deduce the private key if you know the public key. Public-key systems, such as Pretty Good Privacy (PGP), are becoming popular for transmitting information via the Internet. They are extremely secure and relatively simple to use. The only difficulty with public-key systems is that you need to know the recipient's public key to encrypt a message for him or her. What's needed, therefore, is a global registry of public keys, which is one of the promises of the new LDAP technology. Public key cryptography was invented in 1976 by Whitfield Diffie and Martin Hellman. For this reason, it is sometime called Diffie-Hellman encryption. It is also called asymmetric encryption because it uses two keys instead of one key (symmetric encryption).

SET - Short for Secure Electronic Transaction, a new standard that will enable secure credit card transactions on the Internet. SET has been endorsed by virtually all the major players in the electronic commerce arena, including Microsoft, Netscape, Visa, and Mastercard. By employing digital signatures, SET will enable merchants to verify that buyers are who they claim to be. And it will protect buyers by providing a mechanism for their credit card number to be transferred directly to the credit card issuer for verification and billing without the merchant being able to see the number.